## Slide 1
COMPLETE VERSION EVOLUTION REPORT
NX Feature Extractor
v1.0 → v2.0 → v3.0 → v4.1
v1
v2
v3
v4.1
From 9 feature types to 25+ | 60% to 90%+ accuracy | 7 versions | Zero guesses
Diagnostic-first methodology — All APIs confirmed by live NX 2506 testing
Siemens NX v2506 • NXOpen Python • Automotive Sheet Metal Grade

## Slide 2
Version Snapshot — At a Glance
Metric | v1.0 | v2.0 | v3.0 | v4.1
Feature types | 9 | 20+ | 20+ | 25+
Architecture | Single classifier | Single classifier | EdgeCache | Multi-engine fusion
Confidence scoring | None | None | None | 8 engines + fusion
Iterator materialised | No | No | Yes (partial) | Yes (complete)
Bore vs Boss | No | Partial | Centroid check | Centroid + context
Annular face | No | No | Yes | Yes + ring width
Fillet size gate | No | No | 10mm gate | 10mm + neighbour check
ISO size mapping | No | No | No | 30 entries + config file
DFM flags | No | No | No | L/D ratio + extensible
Precision labelling | None | None | None | (API)/(calc)/(approx)
Conflict resolution | None | None | None | Tier + specificity
Output formats | TXT+CSV | TXT+CSV | TXT+CSV | TXT+CSV+JSON
Overall accuracy | ~60% | ~55% | ~82% | ~90%+

## Slide 3
Accuracy Evolution — Feature by Feature
Chart: 
| Holes | Fillets | Chamfers | Boss/Bore | Pockets | Slots | Patterns | Small parts
v1.0 | 95 | 70 | 70 | 50 | 0 | 0 | 0 | 60
v2.0 | 95 | 40 | 70 | 50 | 30 | 40 | 50 | 0
v3.0 | 97 | 85 | 82 | 80 | 75 | 70 | 85 | 60
v4.1 | 98 | 90 | 85 | 85 | 80 | 75 | 90 | 70
v1.0
~60%
v2.0
~55%
v3.0
~82%
v4.1
90%+
Note: v2 accuracy lower than v1 — new heuristics introduced more misfires than features gained. Fixed in v3.

## Slide 4
Architecture Evolution
v1.0
Single Classifier
Face type switch
Hardcoded v1 APIs only
No caching
Linear scan
v2.0
Expanded Classifier
+ 20+ feature types
+ is_edge_curved() (slow)
- Double GetFaces() call
- Iterator exhaustion bug
v3.0
EdgeCache + Gates
+ Single NX pass per face
+ Size/area gate filters
- list() materialisation
- Confidence missing
v4.1
Multi-Engine Fusion
+ 8 independent engines
+ BodyCache (body-level)
+ Confidence + tier scores
+ Conflict resolution

## Slide 5
Bug History & Fix Timeline
v2
HIGH
GetHoleData() returns metres not mm
v2
×1000 conversion applied
v2
HIGH
edge.EdgeType.value = class ref not int
v3
Length-ratio heuristic replaces
v2
HIGH
AskFaceUvMinMaxValues not available
v3
Cross-product normal workaround
v3
CRITICAL
body.GetFaces() iterator exhausted
v3
list() materialisation
v3
HIGH
Annular face → POCKET misfire
v3+
Concentric radius detection
v3
HIGH
Body curves → FILLET (r=50mm)
v3
10mm size gate
v3
HIGH
92 cylinders → BOSS not BORE
v3
Centroid distance check
v4
CRITICAL
TYPE_SPECIFICITY key never matches
v4.1
Full type string lookup
v4
SAFETY
GetBlendData None crash risk
v4.1
None guard added
v4
INTEGRITY
Fake 'exact' precision labels
v4.1
(API)/(calc)/(approx) labels
v4
ACCURACY
Variable-radius fillet wrong
v4.1
BodyCache neighbour check
ver severity bug description fixed_in solution

## Slide 6
NEXT PHASE
GD&T Automation
Module 2
Tolerance Rule Engine
Map each feature type to ISO/ASME tolerance. Toggle between standards. Sheet metal DFM rules.
Module 3
NX PMI Writer
Apply GD&T annotations directly in NX 3D workspace. Datum A/B/C, true position, flatness, angularity.
Module 4
ISO / ASME Toggle
Single button switches between ISO GPS and ASME Y14.5. All tolerance values update automatically.
Module 5
Report Generator
Export annotated model with full GD&T report. PDF + 3D PMI model + inspection checklist.